## Slide 1: Assembly Language Lecture #4: Arithmetic
Notes prepared for COMP 7615 (Carly Orr)
References and select slides from:
Computer Organization and Architecture (Stallings, 2016)
Structured Computer Organization (Tanenbaum, 2013)
http://www.nasm.us/doc/nasmdoc3.html (NASM Document)

## Slide 2: Test Your Understanding
Is NASM case sensitive?
What is the difference between MOV ax, foo versus MOV ax, [foo]?
How many bytes will this data declaration generate? (hint: “times” means allocate 10 words, each initialized to zero).
table times 10 dw 0

## Slide 3
Review:
 x86 registers (week2 slides)
 addressing modes (week3 slides)
Arithmetic
 must recognize registers

## Slide 4: Arithmetic – “add” and “sub”
Both instructions can be used for a pair of signed numbers, or a pair of unsigned numbers.
- two’s complement advantage
- no mixing signed and unsigned
CPU has no idea if signed or unsigned
- you keep track
- cpu happily add whatever registers together using binary addition
Some flags may be set, as a result:
the carry bit
the overflow bit
the zero bit (=1 if result is zero)
the sign bit (=1 if result is negative)

## Slide 5: Immediate Addressing
Data has a constant value, or an expression.
Typically, first operand is register or memory location, and second operand is immediate.
First operand defines length of data.
Examples: ADD var, 65 ;an immediate operand 65 is added
MOV AX, 45h ;immediate constant 45h is transferred
Immediate data forms:

## Slide 6: Overflow?
What is it?
When data is “out of range”
A register has “limited number of bits”
It is your job to check!!
How do we detect overflow?
For unsigned numbers: if carry it is set, we have overflow
For signed numbers: if overflow bit is set, we have overflow

## Slide 7: Multiplication
mul
Unsigned number multiplication
Imul
Signed number multiplication
Why two instructions?
Consider the multiplication of FF by FF - If we assume unsigned quantities, this is 255*255 = 65035 = FE0Bh
- If we assume signed quantities, this is -1 * -1 = 1 = 0001h

## Slide 8: The “imul” instruction
Imul, which is used for signed numbers, has three formats:
imul src
imul dst, src1
imul dst, src1, src2

## Slide 10: Division – integer division
div
Unsigned number multiplication
idiv
Signed number multiplication
Format:
div/idiv src
Example:
19/4 produces
quotient 4
remainder 3

## Slide 11: Negation
neg
Computes 2’s complement
Works on 8, 16, 32 bit
Works on registers or memory

## Slide 12: Conclusion
One must be careful doing arithmetic because the CPU happily produces results, but it may be “bogus”.
Check your carry and overflow bits!