Comp 8006 Assignment 2

Network Emulator

By: Peyman
& John Warren

For: Aman Abdulla

Due: Feb 15, 2018
Table of Contents

Design Work

Objective
To design, implement and test a standalone Linux firewall and packet filter
Usage
Firewall
Run with root access ./fw0.sh
Client
Run with root access ./client_setup.sh

Specifications
1 - use netfilter
2 - load user configuration for all forwarded traffic
3 - set default policies for firewall
4 - dns, dhcp enabled
5 - in/out tcp/udp ports, icmp types
6 - default rule = drop
7 - reject wrong way (i.e. syn in on high ports)
8 - accept fragments
9 - drop tcp with SYN & FIN set
10 - no telnet packets allowed
11 - block external
111, 137-139, 515, 32768-32775
12 - ftp/ssh minimum delay,
13 - ftp max thruput
14 - first [en01] = outside, second [enp3s2] = inside
15 - test procedure; test rules, print results (log)
16 - need to know which rule passed/failed
17 - Allow user to define own rules
18 – separate file for config
19 – define network interfaces
20 – define allowed tcp, udp, icmp
21 – stateful filtering

Set up

State Machine

Pseudo Code
User Variables
1 – Provide variables to allow user to define values for internal and external interfaces, subnets and IP addresses.
2 – Allow user to define what ports to allow for udp and tcp and icmp types

Configure Firewall
1. Backup existing configuration
2. configure network cards
3. Flush existing configuration
4. apply default rule and drop all packets
5. define chains
6. apply user rules, assigning chains for each of tcp, udp, icmp
  1. for each port, apply rule, add to chain

Configure client
1. Backup current config
2. Disable primary network
3. Connect network cable
4. Configure internal network card
Test Plan & Results
Usage ‘./test.sh <IP of target>’ on either client for outbound or another machine on the network for inbound

Inbound
Testing	Test method	expected	Result
TCP port 22	hping3 ip -V -S -p 22 -c 1	ALLOWED	PASS
TCP port 80	hping3 ip -V -S -p 80 -c 1	ALLOWED	PASS
TCP port 443	hping3 ip -V -S -p 443 -c 1	ALLOWED	PASS
UDP port 53	hping3 ip -V –udp -S -p 53 -c 1	ALLOWED	FAILED
UDP port 67	hping3 ip -V –udp -S -p 67 -c 1	ALLOWED	FAILED
UDP port 68	hping3 ip -V –udp -S -p 68 -c 1	ALLOWED	FAILED
ICMP port 0	hping3 ip -V -1 -S -p 0 -c 1	ALLOWED	FAILED
ICMP port 8	hping3 ip -V -1 -S -p 8 -c 1	ALLOWED	FAILED
TCP port 23	hping3 ip -V -S -p 23 -c 1	DROPPED	PASS
TCP port 111	hping3 ip -V -S -p 111 -c 1	DROPPED	PASS
TCP port 137	hping3 ip -V -S -p 137 -c 1	DROPPED	PASS
TCP port 138	hping3 ip -V -S -p 138 -c 1	DROPPED	PASS
TCP port 139	hping3 ip -V -S -p 139 -c 1	DROPPED	PASS
TCP port 515	hping3 ip -V -S -p 515 -c 1	DROPPED	PASS
TCP port 32768	hping3 ip -V -S -p 32768 -c 1	DROPPED	PASS
TCP port 32775	hping3 ip -V -S -p 32775 -c 1	DROPPED	PASS
UDP port 23	hping3 ip -V –udp -1 -S -p 0 -c 1	DROPPED	PASS
UDP port 111	hping3 ip -V –udp -1 -S -p 8 -c 1	DROPPED	PASS
UDP port 137	hping3 ip -V –udp -S -p 23 -c 1	DROPPED	PASS
UDP port 138	hping3 ip -V –udp -S -p 111 -c 1	DROPPED	PASS
UDP port 139	hping3 ip -V –udp -S -p 137 -c 1	DROPPED	PASS
UDP port 515	hping3 ip -V –udp -S -p 138 -c 1	DROPPED	PASS
UDP port 32768	hping3 ip -V –udp -S -p 139 -c 1	DROPPED	PASS
UDP port 32775	hping3 ip -V –udp -S -p 515 -c 1	DROPPED	PASS
ICMP port 200	hping3 ip -V -1 -S -p 200 -c 1	DROPPED	PASS
TCP SPOOF	hping3 ip -V -c 1 -S -s 80 -p 80 --spoof 192.168.10.5	DROPPED	PASS
TCP SYN FIN	hping3 ip -V -c 1 -s 1000 -p 80 -SF	DROPPED	PASS
UDP fragment	hping3 ip -V -S -p 22 -c 1 -f	DROPPED

SSH in - Connected

Outbound
Testing	Test method	expected	Result
TCP port 22	hping3 ip -V -S -p 22 -c 1	ALLOWED	PASS
TCP port 80	hping3 ip -V -S -p 80 -c 1	ALLOWED	PASS
TCP port 443	hping3 ip -V -S -p 443 -c 1	ALLOWED	PASS
UDP port 53	hping3 ip -V –udp -S -p 53 -c 1	ALLOWED	PASS
UDP port 67	hping3 ip -V –udp -S -p 67 -c 1	ALLOWED	PASS
UDP port 68	hping3 ip -V –udp -S -p 68 -c 1	ALLOWED	PASS
ICMP port 0	hping3 ip -V -1 -S -p 0 -c 1	ALLOWED	PASS
ICMP port 8	hping3 ip -V -1 -S -p 8 -c 1	ALLOWED	PASS
TCP port 23	hping3 ip -V -S -p 23 -c 1	DROPED	PASS
TCP port 111	hping3 ip -V -S -p 111 -c 1	DROPED	PASS
TCP port 137	hping3 ip -V -S -p 137 -c 1	DROPED	PASS
TCP port 138	hping3 ip -V -S -p 138 -c 1	DROPED	PASS
TCP port 139	hping3 ip -V -S -p 139 -c 1	DROPED	PASS
TCP port 515	hping3 ip -V -S -p 515 -c 1	DROPED	PASS
TCP port 32768	hping3 ip -V -S -p 32768 -c 1	DROPED	PASS
TCP port 32775	hping3 ip -V -S -p 32775 -c 1	DROPED	PASS
UDP port 23	hping3 ip -V –udp -1 -S -p 0 -c 1	DROPED	PASS
UDP port 111	hping3 ip -V –udp -1 -S -p 8 -c 1	DROPED	PASS
UDP port 137	hping3 ip -V –udp -S -p 23 -c 1	DROPED	PASS
UDP port 138	hping3 ip -V –udp -S -p 111 -c 1	DROPED	PASS
UDP port 139	hping3 ip -V –udp -S -p 137 -c 1	DROPED	PASS
UDP port 515	hping3 ip -V –udp -S -p 138 -c 1	DROPED	PASS
UDP port 32768	hping3 ip -V –udp -S -p 139 -c 1	DROPED	PASS
UDP port 32775	hping3 ip -V –udp -S -p 515 -c 1	DROPED	PASS
ICMP port 200	hping3 ip -V -1 -S -p 200 -c 1	DROPED	PASS
TCP SPOOF	hping3 ip -V -c 1 -S -s 80 -p 80 --spoof 192.168.10.5	DROPPED	PASS
TCP SYN FIN	hping3 ip -V -c 1 -s 1000 -p 80 -SF	DROPPED	PASS
UDP fragment	hping3 ip -V -S -p 22 -c 1 -f	DROPPED

SSH out test